PETROL INJECTION COMPONENTS TR5-6

Parts Required to Convert a Non Petrol Injected TR5/TR250/TR6 to Petrol Injection (P.I.)

NOTE 1:

This sheet presupposes that the vehicle has never had P.I.  If the car was originally P.I. some items such as fuel runs and petrol tank may not be required.

NOTE 2:

Any 6 cylinder Triumph can be made to run on P.I., however the metering unit (MU) will require calibration if the cam, cylinder head, and exhaust are non-standard.

NOTE 3:

Part numbers and descriptions are those appropriate to a CP TR6 unless otherwise stated.  If CR TR6 or 2.5 P.I. manifolds for instance are to be used, or TR5 petrol line runs are required, there will be specific part number changes - please phone to discuss.

NOTE 4:

Only certain cylinder heads will accept injection manifolds.  Early TR6 carb and TR250 are not acceptable.

NOTE 5:

We cannot guarantee the availability of parts, either new or second-hand at any given time; therefore new parts may have to be substituted for second-hand and vice versa as appropriate.

NOTE 6:

Revington TR can fit all the equipment at their premises.  As a guide approximately 40 hours is required to fit and set up the equipment. Labour rate £please enquire.

### The following list covers most parts required: -

| QTY | PART NUMBER | DESCRIPTION |
| --- | --- | --- |
| 1 | 308396 | Pedestal supporting metering unit |
| 2 | 145720 | Seals in pedestal |
| 1 | AJM682 | Manifold gasket |
| 3 | 152807 | Manifold CP (with S/H spindle etc) |
|  | OR |  |
| 3 | 308292 | Manifold CR (with S/H spindle etc) |
| 6 | 152601 | Hose to air manifold |
| 4 | GHC1217 | Clip to air manifold |
| 1 | 216374 | Air manifold |
| 1 | 214840 | Air manifold stay |
| 1 | 149693 | Hose to air filter |
| 1 | 149306 | Air cleaner support |
| 1 | 308444SS | Air cleaner assy (new are stainless steel) |
| 1 | GFE1048 | Air cleaner |
| 1 | 312529 | Metering unit (MU) CP |
|  | OR |  |
| 1 | 312529EX | MU exchange |
| 1 | UKC351SET | Injector pipes set plastic, set of 6 |
|  | OR |  |
| 1 | RTR4107 | Stainless steel injector pipes set of 6 |
| 2 | 518630 | Banjo bolt (injector leads 2 & 6) |
| 6 | 157913 | Injector push in. New |
|  | OR |  |
| 6 | 157913EX | Injector push in Exchange |
| 3 | 149308 | Injector plate |
|  | OR |  |
| 6 | RTR4096 | Injector plate stainless steel |
| 1 | 149595 | Coupling MU |
| 1 | 149005 | Throttle cable |
| 1 | 214888Z | Double choke cable round knob |
|  | OR |  |
| 1 | UKC5240 | Double choke cable square knob |
| 1 | 149604 | Countershaft throttle assy |
|  | OR |  |
| 1 | RTR4211K | Modified throttle actuating kit |
| 1 | 214420 | Throttle pedal RHD |
|  | OR |  |
| 1 | 159877 | Throttle pedal LHD |
| 1 | 312359XALK | Aluminium petrol tank |
| 1 | PPS6E | Petrol pipe set |
| IF WISHING TO USE THE LUCAS PUMP USE THE FOLLOWING COMPONENTS: |
| 1 | 215299 | Filter assy |
| 1 | 151204X | Pipe tank to filter |
| 1 | 149556 | Pipe filter to pump |
| 1 | 151229 | Pipe PRV to filter |
| 1 | 214347 | Petrol pump new |
|  | OR |  |
| 1 | 214347EX | Petrol pump exchange (including surcharge) |
| 3 | UKC2451 | Petrol pump mount |
| IF USING OUR BOSCH CONVERSION, THIS COMES AS A KIT INCLUDING HOSES: |
| 1 | RTR4050K | Bosch petrol pump kit in the boot |
|  | OR |  |
| 1 | RTR4050XK | Bosch petrol pump kit outside |
| THE FOLLOWING PARTS ARE COMMON TO BOTH PETROL PUMP INSTALLATIONS: |
| 1 | 215642 | Hose pump to PRV |
|  |  | OR |
| 1 | 215642SS | Hose pump to PRV (not for use with RTR4001 Bosch kit) |
|  |  | OR |
| 1 | RTR4048 | Hose pump to PRV (for use with our Bosch Kit) |
| 1 | 149773 | 'T' piece holding PRV |
| 2 | UKC2451 | Mounting 'T' piece to body |
| 1 | 156160 | Strainer & pressure relief valve (PRV) |
| 1 | 149767 | Union between feed pipes |
| 1 | 214890 | Hose to metering unit |
|  | OR |  |
| 1 | 214890SS | Hose to metering unit stainless steel |
| 1 | 148947 | Elbow hose return from MU |
|  | OR |  |
| 1 | 217841SS | Elbow hose return from MU stainless steel |
| 1 | RTR4017K | Relay kit for pump feed |
| 1 | C41220A | Inertia cut out switch |
| 1 | C41220ACL | Inertia cut out switch clip |
| 1 | 626717 | Badge 'Injection' |
| 1 | 214459EX | Lucas 41219 'PI' distributor exchange |

Please use our website www.revingtontr.com for current prices